## Slide 1
Hydrorock
Highway Filter Drains
www.hydrorock.com

## Slide 2
Hydrorock Highway Filter Drain System - Option 1:
Eliminates need for Temporary Works (i.e. no shoring-up)
~ 15% more soil excavation (volume & weight)
~ 60% less infill weight (far fewer vehicle loads with Hydrorock)
~ 110% more water storage capacity (over double capacity)
~ 40% bigger Infiltration Surface Area (much more efficient than gravel system)
30 year filter life (double gravel 15 year filter life)
Free recycling by Rockwool (gravel needs expensive cleaning)
System Design:
Excavation dimensions – 1000mm wide x 1200mm deep
Actual System dimensions – 800mm wide x 1200mm deep
Hydrorock Blocks D170 HDX
  Each @ 1200mm L x 400mm W x 500mm H (38.4kg)
  Each @ 220 L storage capacity
Extra-High Density Hydrorock Blocks (160kg / m3) with GeoGrids lifts loading capacity to Ultra-High Density (200kg / m3)
Storage capacity per linear metre – 704 L
Gravel
Hydrorock
Excavation Depth
Excavation Width
Water Storage Capacity
1500mm
1200mm
750mm
1000mm
338L
704L (Blocks & gravel)
System Comparison – Gravel Vs Hydrorock per linear metre:
Excavation Volume / weight
1.13m3 / 1.7t
1.8m3 / 1.44t
Material infill weight
~0.7t (Blocks & gravel)
1.9t
Gravel (20mm +)
Drainage Sand or
Pea Shingle
Geotex membrane
GeoGrid
100mm
Geogrid 40mm high
gravel filled & on top
100mm
1000mm
800mm
1000mm
D220 HDX
D220 HDX
D220 HDX
D220 HDX
NB. Assumed soil weight 1.5t/m3 - Assumed gravel weight 1.68t/m3
Infiltration Surface Area
1.5m2
2.1m2

## Slide 3
Hydrorock Highway Filter Drain System - Option 2:
Eliminates need for Temporary Works (i.e. no shoring-up)
~ 15% less soil excavation (volume & weight)
~ 60% less infill weight (far fewer vehicle loads with Hydrorock)
~ 95% more water storage capacity (almost double capacity)
~ 33% bigger Infiltration Surface Area (much more efficient than gravel system)
30 year filter life (double gravel 15 year filter life)
Free recycling by Rockwool (gravel needs expensive cleaning)
System Design:
Excavation dimensions – 800mm wide x 1200mm deep
Actual System dimensions – 600mm wide x 1200mm deep
Hydrorock Blocks D170 HDX
  Each @ 1200mm L x 300mm W x 500mm H (28.8kg)
  Each @ 170 L storage capacity
Extra-High Density Hydrorock Blocks (160kg / m3) with GeoGrids lifts loading capacity to Ultra-High Density (200kg / m3)
Storage capacity per linear metre – 652 L
Gravel
Hydrorock
Excavation Depth
Excavation Width
Water Storage Capacity
1500mm
1200mm
750mm
800mm
338L
652L (Blocks & gravel)
System Comparison – Gravel Vs Hydrorock per linear metre:
Excavation Volume / weight
1.13m3 / 1.7t
0.96m3 / 1.44t
Material infill weight
~0.7t (Blocks & gravel)
1.9t
Gravel (20mm +)
Drainage Sand or
Pea Shingle
Geotex membrane
GeoGrid
100mm
Geogrid 40mm high
gravel filled & on top
100mm
1000mm
600mm
800mm
D170 HDX
D170 HDX
D170 HDX
D170 HDX
NB. Assumed soil weight 1.5t/m3 - Assumed gravel weight 1.68t/m3
Infiltration Surface Area
1.5m2
2.0m2

## Slide 4
Hydrorock Highway Filter Drain System - Option 3:
Eliminates need for Temporary Works (i.e. no shoring-up)
~ 30 % less soil excavation (volume & weight)
~ 60% less infill weight (far fewer vehicle loads with Hydrorock)
~ 65% more water storage capacity
~ 22% bigger Infiltration Surface Area (more efficient than gravel system)
30 year filter life (double gravel 15 year filter life)
Free recycling by Rockwool (gravel needs expensive cleaning)
Gravel (20mm +)
Drainage Sand or
Pea Shingle
Geotex membrane
GeoGrid
100mm
Geogrid 40mm high
gravel filled & on top
100mm
830mm
600mm
800mm
System Design:
Excavation dimensions – 800mm wide x 1030mm deep
Actual System dimensions – 600mm wide x 1030mm deep
Hydrorock Blocks D112 HDX
  Each @ 1200mm L x 300mm W x 330mm H (19kg)
  Each @ 112 L storage capacity
Hydrorock Blocks D170 HDX
  Each @ 1200mm L x 300mm W x 500mm H (28.8kg)
  Each @ 170 L storage capacity
Extra-High Density Hydrorock Blocks (160kg / m3) with GeoGrids lifts loading capacity to Ultra-High Density (200kg / m3)
Storage capacity per linear metre – 560 L
D112 HDX
D112 HDX
D170 HDX
D170 HDX
Gravel
Hydrorock
Excavation Depth
Excavation Width
Water Storage Capacity
1500mm
1030mm
750mm
800mm
338L
560L (Blocks & gravel)
System Comparison – Gravel Vs Hydrorock per linear metre:
Excavation Volume / weight
1.13m3 / 1.7t
0.82m3 / 1.23t
Material infill weight
~0.65t (Blocks & gravel)
1.5m2
NB. Assumed soil weight 1.5t/m3 - Assumed gravel weight 1.68t/m3
Infiltration Surface Area
1.9t
1.83m2